## Slide 1: PONG
ELEC5620M Project Demonstrator
John Jakobsen (201291841)
Sam Wilcock (201285260)
Alexander Bolton (200938078)

## Slide 2: Introduction
One of the earliest arcade games
Different varieties exist (singleplayer, multiplayer)
Displays the range of skills gained in the module
Uses VGA, LCD, buttons, HEX display, PS/2

## Slide 3: Physics
  Collision checks are carried out in the
  while loop
  Border collisions invert the angle
  Paddle collisions change the angle and
  speed according to the collision location

## Slide 4: Display Driver
  320 x 240 pixels
  Frame buffer made up of two types of arrays
  Frame skip feature added
  Functions added to the engine to ease use

## Slide 5: Sprites & Text
Ball generated using Pythagoras’ theorem
Paddles created using Bresenham algorithm
Text made using a library of hex values

## Slide 6: Game Engine
Sprite location recorded by global values
Sprites created and destroyed with commands in the game engine
Angle calculated using Bresenham algorithm

## Slide 7: Menus
Three main types of screen
Menu contains blocking and non-blocking elements
Allows user to change audio, paddle size and game mode

## Slide 8: Controls
Implementation of slider switches
Usage of interrupts
Macros created to aid functioning of inputs

## Slide 9: Audio
Uses fast sin function
Values of sin(θ) calculated in Matlab and copied into a lookup table
Header file created containing musical notes